## Slide 1: Proposal to Change the UNC AQ ‘Backstop Date’ to accommodate the 2010 Seasonal Normal Review DESC – 2nd October 2009 NOTE: Instances where TBC is stated in the slides is pending analysis completion (post 01/10/09). This data will be available for DESC or as a post meeting update
<number>
Notes: <number>

## Slide 2: Background
<number>
Outputs from the 2010 Seasonal Normal (SN) Review are:
  Revised SNCWVs, ALP, DAF and EWCF parameters
    Adjusted to the new SN basis
Revised values will be used in the calculation of future and historical Weather Adjusted Annual Load Profiles (WAALP)
WAALPs are subsequently used in the calculation of AQs
  Adjusting the relevant metered quantity of the AQ to a SN value
    Representative of expected consumption under average conditions
Notes: <number>

## Slide 3: AQ Calculation & WAALPs
<number>
AQ Calculation defined in UNC (H3.4)
RMQ represents the Relevant Metered Quantity
The remaining part of the calculation is termed the WAALP
  WAALP represents the adjustment of AQs to SN (UNC H3.1.1)
SNCWV is incorporated into the EWCF parameter
Notes: <number>

## Slide 4: AQ Calculation – Historical WAALPs
<number>
KEY: AQ calculations are based on historical consumption that is used to represent a view of expected consumption in the next 12 months adjusted to SN
IMPACT: Historical WAALP values have to be recalculated to the new SN basis to allow all AQs that are effective from 01/10/10 (latest SN Review) to be reflective of new basis.
WAALP values are recalculated to new SN basis using the most recent Demand Estimation demand models i.e. from 2008/09 to apply 2009/10 (UNC H3.4.3)
The recalculated values will be used in March 2010 (onwards) AQ Review calculation processes for AQs going live on 01/10/10
Notes: <number>

## Slide 5: AQ Calculation – WAALPs and Non-Calculated AQs
<number>
For AQs that are not calculated (i.e. Carry Forward AQs)
  A multiplicative factor per EUC will be applied to the current AQ value to adjust from the old SN basis to the new SN basis
  Defined in UNC H3.4.4 (AQ = (Current AQ x (A/B))
    e.g. An AQ of 20,000 kWh in EUC Band 1
    Adjusted by multiplying difference between the old aggregate WAALP (356) and the new aggregate WAALP (352)
    Result 0.9888
    AQ to be effective from 01/10/10 on the new basis is 19,776 kWh
Notes: <number>

## Slide 6: Timeline to Derive and Implement WAALPs
<number>
SNCWV’s will be derived and finalised by the end of December 2009
The historical WAALP values are derived by re-running the latest Demand Estimation demand models (UNC H3.4.3)
Process takes place in January & February 2010
  Latest Gas Year data has to be available to derive new values and new SNCWV values will not available until end of December 2009
New WAALP values up to February 2010 are loaded into Transporter systems during March 2010
  Ongoing daily calculation and loading of WAALPs for March 2010 – September 2010 takes place
AQ calculation (SSP) takes place in March 2010 (LSP – April)
  Utilising historical WAALP values and metered quantity
Notes: <number>

## Slide 7: Issues
<number>
1. Timescales are tight to derive the new SNCWV and parameters based on the new SN basis
  Most recent demand models have to be re-run to derive the new values
  Timescales allow WAALP values to be derived using the latest models calculating back to 01/10/2006
  Calculating additional historical WAALPs would require significant additional modelling as the models being used (as per UNC) only utilise data post 01/10/06
2. Models used to back calculate new WAALPs are based on data pertaining to 01/10/06 onwards (06/07, 07/08 and 08/09)
  Using these models to derive WAALPs for any period prior to 01/10/06 could be deemed as inappropriate
  Models not representative of the period prior to 01/10/06
Therefore WAALP data will only be available back to 01/10/2006 for AQ calculations
Notes: <number>

## Slide 8: Impact
<number>
UNC (H3.2.3) currently states that AQs can be calculated using meter reads back to to 01/10/2002
  Commonly referred to as the AQ ‘backstop date’
  No consumption history prior to this date can be used
  This was changed to 01/10/2002 in 2005 (Modification 0018)
  Changed due to similar issue arising in the 2005 SN Review
As a result of UNC, systems would currently have to have WAALP data back to 01/10/2002
Conflict – what is possible and appropriate with what is required in UNC
If AQs are calculated using the old (or a mixed) SN basis
+
  SN basis is anticipated to create warmer SNCWVs
  Old basis WAALPS creates AQs that are too high (allocation, charging, rec. etc)
  Would not adhere to UNC (two SN basis)
Notes: <number>

## Slide 9: Illustration of Relevant UNC Text
<number>
Relevant UNC Section H3.2:
3.2.3 The starting Meter Read shall be:
    (a) the latest Valid Meter Read before the target opening date, or if there was no such Meter Read less than three years before the target opening date;
    (b) subject to paragraph 3.2.4, the first Valid Meter Read after the target opening date.
  Provided always that the starting Meter Read shall be no earlier than 1 October 2002
3.2.4 If there was no Valid Meter Read less than three years before the target opening date or more than 6 months before the ending Meter Read, or the first Valid Meter Read after the target opening date was earlier than 1 October 2002, paragraph 3.1.2 shall apply.
Fixing a date in UNC is not a preferable option
  Same issue will arise in the future
Notes: <number>

## Slide 10: Proposal
<number>
Proposal:
  Change the AQ backstop date in UNC from 01/10/2002 to be
    Start of the gas year in which a Seasonal Normal Review becomes effective (01/10/xx) – 4 years
      e.g. 01/02/10 backstop becomes 01/10/06
      e.g. 01/02/15 backstop becomes 01/10/11
    Change to be effective 1st February the preceding year
  Therefore backstop date would be
    At its shortest point (February prior to SN change effective year) 3 years 4 months
    At its longest point (January prior to SN change effective year) 8 years 4 months
  To illustrate…
UNC SECTION H3.2
Notes: <number>

## Slide 11: Proposal - Illustrative Example
<number>
AQ Review calculation is able to take place in March using the new WAALP data back to 01/10/06 for AQs to be effective from 01/10/10 (on the new SN basis)
1. Current UNC AQ Backstop Date
Is fixed as 01/10/2002
(UNC Section H3.2.3 and 3.2.4)
2. New Seasonal Normal Basis due to be effective from Effective Date 01/10/10 (start of new Gas Year)
4. New AQ Backstop Date becomes 01/10/2006
3. 1st February 2010
AQ backstop Date is changed to
New SN Basis Effective Date – 4 Years
e.g. 01/10/10 – 4 = 01/10/06
Key Point - Change to backstop date has to be undertaken prior to March to allow use of the WAALP data in the AQ calculation
Notes: <number>

## Slide 12: Proposal Requirements
<number>
Requirements: UNC Modification to be raised, reviewed and if agreed, implemented by 12th February 2010 (4 months from today)
  New SNCWV and model back calculating takes place in Jan-Feb 2010
  New WAALPs derived in Feb 2010
  21+ million backstop dates amended during February 2010 by March 2010
  Revised WAALP data would then need to be loaded in March 2010
  SSP AQ calculation takes place end March 2010 (LSP takes place end of April 2010)
Notes: <number>

## Slide 13: Analysis of Impacts of Proposal
<number>
Detailed analysis has been undertaken
  Impacts cannot be fully assessed as this would require a change to the backstop date in the system and run of the AQ calculation process
  Provide as much detail and anticipated view of impact as possible to support industry understanding
1.5 million Meter Points do not have a consumption history post 01/10/06 that could be impacted
  xx% (tbc) of these did not calculate in 2009 as not part of a Live Confirmation / other reason
Further more this will be reduced by:
  Rules within UNC (H3.2) regarding the ‘Relevant Metered Period’ (period for an AQ calculation)
  Comparison of impacts from last backstop date change in 2005
  Review of AQ 2009 calculations
  Overview of AQ calculation validation process
Analysis indicates that the anticipated impact of backstop date change will be small…
Notes: <number>

## Slide 14: Analysis of Impacts of Proposal
<number>
1. Although 1.5 million Meter Points that do not have a consumption history post 01/10/06 currently
  Further reads will be provided between now and AQ Review 2010
  xoserve receive approximately 1.5 million reads per week
  This would equate to an additional 30 million reads between October 2009 and March 2010
    These reads should be after 01/10/2006
      Annual Read Meters – once every 24 months (UNC M3.5.1 (a))
      Monthly Read Meters – once every 4 months (UNC M3.4.1 (a))
2. As per UNC Section H3.2 – reviewing the Relevant Metered Period
  i.e. the period of consumption data that can be used in an AQ calculation…
Notes: <number>

## Slide 15: AQ Backstop Date Change – Relevant Metered Period in AQ 2010 System Calculation - Approximate ‘Worst Case Scenario’
<number>
3. 14th March 2008
Maximum time between NDM Annual Meter Reads is 24 months (M3.5.1(a)) i.e. earliest possible ‘ending Meter Read’ (For Monthly Read = 50 weeks = 17th March 2008)
1. 15th March 2010* - AQ 2010 SSP calculation completes
2. 14th March 2010
Last valid reading prior to this point that can be sued in an AQ calculation is the ‘ending Meter Read’
4. 26th May 2007
Target opening date for NDM Annual Read Meters is 42 weeks before ending Meter Read (H3.2.5(b)). The ‘starting Meter Read is the latest reading prior to this date (H3.2.3(a))
(Monthly Read = 17th March 2007)
5. 26th May 2004 (Annual)
Earliest possible date from which to take a starting Meter Read is 3 years prior to Target Opening Date (H3.2.3(a))
(Monthly Read = 17th March 2004)
* Approximate dates (28th March 2010 scheduled date)
Notes: <number>

## Slide 16: Analysis of Impacts and Proposal
<number>
2. cont. Reviewing the Relevant Metered Period
  Earliest consumption date that can be used in the AQ Review 2010 calculation is 17th March 2004
  Current backstop date therefore is no longer appropriate
  The number of Meter Points with an end read on UK Link between 01/03/04 and 30/09/06 is (TBC)
  Deemed to be the maximum number of Meter Points potentially impacted
3. Comparison to 2005 Backstop date change – best comparison
  Backstop was implemented to be 01/10/02 (previously was Meter Point specific)) (Mod 00018)
  At that point - period that could be used in AQ Calculation (01/10/02 to March 2005) was 2 years 5 months
  Period in this proposal (01/10/2006 to 01/02/2010) will be 3 years 4 months (additional year)
Notes: <number>

## Slide 17: Analysis of Impacts of Proposal
<number>
4. Number of Meter Points that did not calculate in 2005 as a result of the backstop date change was 446 (11 SSP, 435 LSP)
  Representing 0.01% of 4.5 million total that did not calculate
  Meter Points primarily fail to calculate for other reasons
    Reasons occurring in time before the AQ backstop date was reached
    Anomalies in asset, meter configuration and / or read histories result in AQ not being calculated
    Backstop date issue becomes secondary issue as these other issues will occur
    2005: 99.9% of all non calculations were due to issues not associated with the backstop date
    2006 to 2009 AQ Review: 99.9% of all non calculations due to issues not associated with the backstop date
    System validates against the following, in the following order…
Notes: <number>

## Slide 18: Analysis of Impacts of Proposal
<number>
Non-Calculated AQs System Validation Order (groupings have been used)
System Validation Order | Reason for AQ Non-Calculation (2009 are provisional values) | Meter Point Count |  | % of Total | 
 |  | 2005 | 2009* | 2005 | 2009*
1 | Meter Point Ownership / Live | 1,116,605 | 1,275,002 | 25% | 30%
2 | Meter Point Configuration (DM / NDM) | 134,339 | 28,284 | 3% | 1%
3 | AQ Backstop Date (01/10/2002) | 446 | 132 | 0% | 0%
4 | Meter Reading Configuration | 98,251 | 102,392 | 2% | 2%
5 | Consumption & Read details | 3,179,989 | 2,780,785 | 70% | 66%
TOTAL |  | 4,529,630 | 4,186,595 | 100% | 100%
Similar values occur each year. Backstop date reduces year to year
Indicates backstop date is not a predominant issue for AQs not being calculated
The 1.5 million previously indicated are anticipated to be in category 1 (85%), 2, 4 and 5
Notes: <number>

## Slide 19: Analysis of Impacts of Proposal
<number>
5. During the 2009 AQ Review for those Meter Points that did re-calculate
    477 Meter Points used a consumption history that was prior to 01/10/06
    Similar to 2005 numbers – feasible similar numbers will apply in 2010
6. When an AQ re-calculation occurs
  AQ backstop date moves to the date of the last read used in the last AQ calculation
    e.g. if an AQ is calculated using read date from 01/05/08 and 01/03/09, the AQ backstop date will move to 01/03/09
  No reads prior to this date will be used in future AQ calculation
  18+ million Meter Points calculated annually using recent consumption
  Majority of Meter Points will have a backstop date post 01/10/2006…
Notes: <number>

## Slide 20: Analysis of Impacts of Proposal - TBC
<number>
Analysis of reads used in AQ Review calculation 2009
  Count of Meter Points with an End Read occurring in (% of total):
    2009: xxxx (xx%)
    2008: xxxx (xx%)
    2007: xxxx (xx%)
    2006 : xxxx (xx%)
    2005 : xxxx (xx%)
    2004 : xxxx (xx%)
    2003 : xxxx (xx%)
Notes: <number>

## Slide 21: Analysis of Impacts of Proposal
<number>
7. AQs should be calculated based on a recent view of consumption data
  Is consumption data pre 01/10/06 representative of the AQ in the preceding Gas Year (G1.6.2(d) / G1.6.6)
  Reads for annual read sites should be obtained every 24 months (UNC section M3.5.1) and monthly reads sites every 4 months (M3.4.1)
    Recent reads should be available
The impact of this option in regards to AQs not being calculated is anticipated to be small
Based on historical analysis and current available information
  Anticipated impact is expected to be of similar proportions or less due to the previous points
Notes: <number>

## Slide 22: Suggested Timeline for Modification
<number>
2nd October Proposal raised & discussed at DESC
15th October UNC Mod raised at UNC Mod Panel
- Consultation or Workstream
22nd October Discuss as Distribution Workstream
10th November Discuss at DESC (if required)
19th November UNC Mod Panel
- Workstream Report & send to Consultation
December Representations Close
17th December UNC Mod Panel send Ofgem determination
11th February (max) Ofgem determination & Implementation
12th February UK Link system update of backstop begins
March UK Link system update complete
NOTE: Worst case scenario UNC Modification Panel could make its decision 21st January 2010
Notes: <number>

## Slide 23: Consequences of not Changing the Backstop Date
<number>
If decision delayed or not implemented:
AQs using history prior to 01/10/06 that are implemented on 1st October 2010 would be calculated on incorrect SN basis
AQ calculations would not adhere to UNC section H3.4.3
AQ values and therefore allocations, reconciliation and transportation charges would be incorrect for these Supply Points
New SN basis expected to introduce warmer SNCWVs therefore smaller AQs
  SSP and LSP AQs using pre 01/10/06 WAALPs will be overstated
Notes: <number>

## Slide 24: Contingency UNC Modification Implemented After February 2010
<number>
Contingencies required if MOD not implemented by 12th February 2010
Proviso that MOD was still implemented prior to April 2010
  Report on sites that have utilised data prior to or crossing 01/10/06 in the 2010 AQ calculation
  Sites would be reviewed by xoserve manually ‘offline’ and options
    1. Recalculated using later reads or
    2. Have their current AQ’s carried forward (and adjusted to the new SN basis)
  Take place during March, April and May 2010 in preparation for May and June notification
  The LSP takes place during April - incorporate similar contingency
  This would adhere to UNC (if Mod implemented by May 2010 / before Shipper notification)
  AQ backstop date would then be amended prior to the Shipper amendment window opening (June 2010)
Notes: <number>

## Slide 25: Contingency UNC Modification not Implemented
<number>
If a Modification not implemented and 01/10/2002 backstop remained:
  All AQs utilising data prior to or crossing 01/10/06 be reviewed and
    1. Recalculated using later reads or
    2. Have their current AQ’s carried forward
  Take place during April and May 2010 in preparation for May notification
  The LSP takes place during April - incorporate similar contingency
  Shipper Appeals or Amendments using pre 01/10/06 data would also incorporate a similar contingency
  xoserve do undertake manual analysis and can decide to carry forward an AQ if it is deemed to be based on inconsistent data
    This would be based on inconsistent SN data so could possibly be carried forward
  An ongoing approach would need to be identified and agreed
Notes: <number>

## Slide 26: Next Steps
<number>
To ensure this is progressed to the timescales required
Welcome DESC thoughts / views / comments on the proposal:
  Change the Backstop date in UNC from 01/10/02 to (start of the gas year in which a Seasonal Normal Review becomes effective) – 4 years
  Change to be effective 1st February of the preceding year
    Timescales to achieve
    Limited anticipated impacts
Notes: <number>