## Slide 1: Modification 0607S: National Grid NTS Actions Update
22nd March 2017

## Slide 2: Action 0202: Provide another worst case scenario based on the Shell low flow period in 2016
The workgroup wanted to understand the impact on the St Fergus blend taking the lowest actual recorded Shell flow over the summer period of 2016
Therefore to calculate the CO2 blend at St Fergus terminal under each of BP’s 4 scenarios, National Grid NTS altered:
  the Shell flow from 18.3 mscm/d to 10.4 mscm/d
  Shell CO2 content from 1.6% to the maximum CO2 limit of 2.0%

## Slide 3: Action 0202: Provide another worst case scenario based on the Shell low flow period in 2016
The results below show an increase above 4% CO2 content entering the NTS under two of the scenarios

## Slide 4: Flow patterns and blending points
In respect of the heat maps, the workgroup requested further information about:
  Assumed distribution of supplies
  Where the gas would blend on the NTS
  NTS flow patterns

## Slide 5: ‘Heat map’ analysis
Five ‘heat map’ schematics are provided:
  The first shows the penetration of aggregate flows of St Fergus gas into the NTS, assuming entry flows are equal to those presented in BP’s analysis, scenario 1
    SAGE: 20 mscm/d
    SEGAL: 18.3 mscm/d
    Vesterled: 8.2 mscm/d
    Frigg: 30 mscm/d
  Scenario 1 was selected because this contains the highest flows of all BP scenarios and is thus a ‘worst case’ from the BP scenarios
  Supplies from other NTS entry points are proportionate to the 2016 FES for that demand level

## Slide 6: ‘Heat Map’ Schematic 1
>75%
St Fergus Gas
50% to 75%
St Fergus Gas
25% to 50%
St Fergus Gas
30/06/2016
(BP Scenario 1)
<25%
St Fergus Gas
8%
45%
9%
30%
2%
1%
1%
3%
1%
The percentages show the contribution to total demand from each supply source
Note: This heat map is a correction to Heat Map 1 in the material provided for the Workgroup meeting 28th February 2017

## Slide 7: ‘Heat map’ analysis
The second shows the penetration of aggregate flows of St Fergus gas into the NTS, assuming entry flows are equal to those presented in BP’s analysis, with SEGAL modified from 18.3 mscm/d to 10.4 mscm/d, otherwise consistent with BP scenario 1
    SAGE: 20 mscm/d
    SEGAL: 10.4 mscm/d
    Vesterled: 8.2 mscm/d
    Frigg: 30 mscm/d
Supplies from other NTS entry points are proportionate to the 2016 FES for that demand level

## Slide 8: ‘Heat Map’ Schematic 2
>75%
St Fergus Gas
50% to 75%
St Fergus Gas
25% to 50%
St Fergus Gas
30/06/2016
(Altered BP Scenario 1)
<25%
St Fergus Gas
13%
40%
9%
30%
2%
1%
1%
3%
1%
The percentages show the contribution to total demand from each supply source

## Slide 9: ‘Heat map’ analysis
The third ‘heat map’ schematic shows the levels of CO2 on the NTS, assuming
  St Fergus sub-terminal flows and CO2 content are equal to BP’s scenario 4 (giving a ‘worst case’ CO2 entering the NTS from the four BP scenarios)
    This scenario shows a blend of 3.87% CO2 entering the NTS, therefore no NTS direct connect receives any gas in excess of 4% (Action 0101 c))
  Supplies from other NTS entry points are proportionate to the 2016 FES for that demand level and deliver gas at their CO2 limits*
* Teesside terminals have been assumed to flow at 4%

## Slide 10: ‘Heat Map’ Schematic 3
>4%
CO²
Gas
3% to 4%
CO²
Gas
2.5% to 3%
CO²
Gas
30/06/2016
(BP Scenario 4)
13%
40%
9%
30%
2%
1%
1%
3%
1%
The percentages show the contribution to total demand from each supply source
Note: This is the same schematic as heat map 2 in the Workgroup material for the 28th February 2017 meeting

## Slide 11: ‘Heat map’ analysis
The fourth ‘heat map’ schematic shows the levels of CO2 on the NTS, assuming
  St Fergus sub-terminal flows and CO2 content are equal to BP’s scenario 4 (giving a ‘worst case’ CO2 entering the NTS from the four BP scenarios), but with SEGAL flows reduced to 10.4mscm/d and a CO2 level of 2.0%
    This scenario shows a blend of 4.24% CO2 entering the NTS, therefore a number of NTS direct connects would receive gas in excess of 4%
  Supplies from other NTS entry points are proportionate to the 2016 FES for that demand level and deliver gas at their CO2 limits*
* Teesside terminals have been assumed to flow at 4%

## Slide 12: ‘Heat Map’ Schematic 4
>4%
CO²
Gas
3% to 4%
CO²
Gas
2.5% to 3%
CO²
Gas
30/06/2016
(Altered BP Scenario 4)
18%
35%
9%
30%
2%
1%
1%
3%
1%
The percentages show the contribution to total demand from each supply source

## Slide 13: ‘Heat map’ analysis
The fifth ‘heat map’ schematic shows the levels of CO2 on the NTS, as Schematic 4 with:
  Blending points
  Direction of flow

## Slide 14: ‘Heat Map’ Schematic 5
>4%
CO²
Gas
3% to 4%
CO²
Gas
2.5% to 3%
CO²
Gas
30/06/2016
(Altered BP Scenario 4)
18%
35%
9%
30%
2%
1%
1%
3%
1%
Blending Points