## Slide 1: XRN4658 – OTR UNCVR Amendment eChMC – 23rd July 2018

## Slide 2: Implementation Approach
R3 changing UNCVR via XRN3656 (splitting Band 2 into 2 bands) - orange
XRN4658 amends the OTR value in bands 3-11 – blue cells
Lower AQ Band (kWh) | Upper AQ Band (kWh) | Tolerances where read will be accepted | Tolerances where a Read will be Accepted if Submitted within Override Flag (Inner Tolerance) | Outer Tolerance Where Read will be Rejected (Market Breaker)
1 | 1 | 0% - 2,000,000% of AQ/365 x no. of days | 2,000,001% - 7,000,000 % of AQ/365 x no. of days | > 7,000,000% of AQ/365 x no. of days
2 | 100 | 0% - 20,000% of AQ/365 x no. of days | 20,001% - 45,000 % of AQ/365 x no. of days | > 45,000% of AQ/365 x no. of days
101 | 200 | 0% - 10,000% of AQ/365 x no. of days | 10,001% - 25,000% of AQ/365 x no. of days | > 25,000% of AQ/365 x no. of days
201 | 500 | 0% - 4,000% of AQ/365 x no. of days | 4,001% - 55,000 % of AQ/365 x no. of days | > 55,000% of AQ/365 x no. of days
501 | 1,000 | 0% - 2,000% of AQ/365 x no. of days | 2,001% - 25,000 % of AQ/365 x no. of days | > 25,000 % of AQ/365 x no. of days
1,001 | 5,000 | 0% - 400% of AQ/365 x no. of days | 401% - 7,000 % of AQ/365 x no. of days | > 7,000% of AQ/365 x no. of days
5,001 | 10,000 | 0% - 200% of AQ/365 x no. of days | 201% - 2,000 % of AQ/365 x no. of days | > 2,000% of AQ/365 x no. of days
10,001 | 20,000 | 0% - 150% of AQ/365 x no. of days | 151% - 1,100 % of AQ/365 x no. of days | > 1,100% of AQ/365 x no. of days
20,001 | 73,200 | 0% - 300% of AQ/365 x no. of days | 301% - 1,100 % of AQ/365 x no. of days | > 1,100% of AQ/365 x no. of days
73,201 | 732,000 | 0% - 250% of AQ/365 x no. of days | 251% - 1,000 % of AQ/365 x no. of days | > 1,000% of AQ/365 x no. of days
732,001 | 2,196,000 | 0% - 200% of AQ/365 x no. of days | 201% - 1,000% of AQ/365 x no. of days | > 1,000% of AQ/365 x no. of days
2,196,001 | 29,300,000 | 0% - 150% of AQ/365 x no. of days | 151% - 700% of AQ/365 x no. of days | > 700% of AQ/365 x no. of days
29,300,001 | 58,600,000 | 0% - 100% of AQ/365 x no. of days | 101% - 400% of AQ/365 x no. of days | > 400% of AQ/365 x no. of days
58,600,001 | and above | 0% - 100% of AQ/365 x no. of days | 101% - 350% of AQ/365 x no. of days | > 350% of AQ/365 x no. of days

## Slide 3: Implementation Approach
Implementation planned for implementation coincident with R3 (Nov UKL Release)
Implementation of 4658 leverages economies of scale of 3656 testing
  Does not seek to duplicate test scenarios, as 3656 demonstrates that the functional processes utilise the amended value
  Limited unique testing to demonstrate 4658 test scenarios work
  Combined System Test / User Acceptance Test cycle for 4658
If 4658 encounters functional issues, 4658 will be backed out so as to preserve 3656 implementation
4658 will be available in Market Trials by virtue of the common code component for 3656